## Slide 1: Japanese Fuel Efficiency Standard for Heavy Duty Vehicles
Environmental Policy Division,
Road Transport Bureau,
Ministry of Land, Infrastructure, Transport and Tourism,
Japan

## Slide 2
1. Background
2. History of Developing FE Standard
3. Outline of Standard
4. Test Method

## Slide 3
1. Background
2. History of Developing FE Standard
3. Outline of Standard
4. Test Method

## Slide 4: CO2 Emission from Transport Sector in Japan
CO2 emissions from automobiles account for 15% of total emissions in Japan, and these from heavy duty vehicles account for 30% of automobiles.
It is important to reduce CO2 from heavy duty vehicles to achieve Japan’s CO2 reduction target.
Chart: 
2030年まで
重量車 | 70.2642 | 74.0537 | 74.4506 | 75.2643 | 79.7662 | 81.5504 | 82.4403 | 80.5557 | 78.9278 | 78.6872 | 77.4826 | 77.6478 | 74.3439 | 72.8312 | 73.3682 | 72.706 | 73.3248 | 72.0071 | 69.5981 | 65.7614 | 67.6055 | 64.7105 | 63.869 | 63.6206 | 63.7353 | 63.4882 | 62.8031
重量車以外の自動車 | 107.5601 | 114.3707 | 120.4111 | 123.4166 | 127.5606 | 133.7154 | 138.9394 | 141.0645 | 142.7661 | 147.4393 | 147.963 | 152.4018 | 151.7436 | 149.5469 | 144.6707 | 139.7122 | 136.3491 | 135.7667 | 132.0714 | 133.9866 | 132.9706 | 131.5864 | 132.4317 | 128.9686 | 123.9262 | 123.2747 | 121.8979
その他輸送機関 | 25.6439 | 26.6512 | 26.6446 | 26.4199 | 27.308 | 28.6143 | 29.4256 | 31.131 | 29.1447 | 28.7375 | 29.1002 | 28.7699 | 29.1363 | 28.8749 | 27.299 | 27.4188 | 27.5224 | 26.704 | 25.1929 | 23.879 | 23.5538 | 23.0527 | 24.0032 | 24.8615 | 24.8185 | 24.5414 | 24.6279
CO2 emission
（million ton）
240
225
209
1.87 million ton reduction per year
Emission Reduction Target
(▲25% by 2030 compared to 2013)
necessary to reduce 3.64 million ton per year
Heavy duty vehicle
Automobile
(except heavy duty vehicle)
Other transportation
163

## Slide 5
1. Background
2. History of Developing FE Standard
3. Outline of Standard
4. Test Method

## Slide 6: History of Developing Fuel Efficiency Standard
2004 Start to consider the fuel efficiency standard for heavy duty vehicles
2006 Development of the standard
・ Target year : 2015
・ Aim to improve fuel efficiency by 12.2% from 2002
・ Test method : Simulation
・ Combining JE05 mode (simulated urban area) and High-way mode
2010 Add the test method of Idle stop and AT
2012 Start to consider the new fuel efficiency standard for further CO2 emission reduction
2017 Development of the new standard
・ Target year : 2025
・ Strengthen regulation by 13.5% compared to 2015 standard
・ Amend the test method
- running resistance and engine map measurement method

## Slide 7
1. Background
2. History of Developing FE Standard
3. Outline of Standard
4. Test Method

## Slide 8
Japanese standard for HD applies to vehicles using diesel fuel and exceeding 3,500kg. (such as trucks, trailer and buses)
The standard was set for each category according to the vehicle weight for each type.
Scope and category
Category |  |  |  | 2025 Standard value
Truck | T1 | 3.5t<GVW<=7.5t | PL<=1.5t | 13.45
 | T2 |  | 1.5t<PL<=2t | 11.93
 | T3 |  | 2t<PL<=3t | 10.59
 | T4 |  | 3t<PL | 9.91
 | T5 | 7.5<GVW<=8t |  | 8.39
 | T6 | 8t<GVW<=10t |  | 7.46
 | T7 | 10t<GVW<=12t |  | 7.44
 | T8 | 12t<GVW<=14t |  | 6.42
 | T9 | 14t<GVW<=16t |  | 5.89
 | T10 | 16t<GVW<=20t |  | 4.88
 | T11 | 20t<GVW<=25t |  | 4.42
Tractor | TT1 | GVW<=20t |  | 3.31
 | TT2 | 20t<GVW |  | 2.32
Category |  |  | 2025 Standard Value
Route Bus | BR1 | 3.5<GVW<=8t | 7.15
 | BR2 | 8t<GVW<=10t | 6.30
 | BR3 | 10t<GVW<=12t | 5.80
 | BR4 | 12t<GVW<=14t | 5.27
 | BR5 | 14t<GVW | 4.52
Tour Bus | B1 | 3.5t<GVW<=6t | 9.54
 | B2 | 6t<GVW<=8t | 7.73
 | B3 | 8t<GVW<=10t | 6.37
 | B4 | 10t<GVW<=12t | 6.06
 | B5 | 12t<GVW<=14t | 5.29
 | B6 | 14t<GVW<=16t | 5.28
 | B7 | 16t<GVW | 5.14
Trucks and Tractor
Buses

## Slide 9
New fuel efficiency standard for trucks (2025 standard)
Chart: 
| 1 | 1.5 | 2 | 2 | 2.5 | 3 | 3 | 3.5 | 4 | 4 | 4.5 | 5 | 5 | 5.5 | 6 | 6 | 6.5 | 7 | 7 | 7.5 | 8 | 8 | 8.5 | 9 | 9 | 9.5 | 10 | 10 | 10.5 | 11 | 11 | 11.5 | 12 | 12 | 12.01 | 12.5 | 13 | 13 | 13.5 | 14 | 14
2025年度基準案 | 13.4532 | 13.4532 | 13.4532 | 11.9265 | 11.9265 | 11.9265 | 10.591 | 10.591 | 10.591 | 9.9111 | 9.9111 | 9.9111 | 8.3947 | 8.3947 | 8.3947 | 7.4616 | 7.4616 | 7.4616 | 7.4405 | 7.4405 | 7.4405 | 6.4191 | 6.4191 | 6.4191 | 5.8942 | 5.8942 | 5.8942 | 4.8775 | 4.8775 | 4.8775 | 4.4247 | 4.4247 | 4.4247 | 3.1072 | 3.1072 | 3.1072 | 2.3238 | 2.3238 | 2.3238 | 2.3238
2014年度平均燃費値 | 11.67 | 10.6 | 9.44 | 8.62 | 7.5 | 6.67 | 6.64 | 5.77 | 5.24 | 4.37 | 3.99 | 2.92 | 2.16
2015年度基準 | 10.83 | 10.83 | 10.83 | 10.35 | 10.35 | 10.35 | 9.51 | 9.51 | 9.51 | 8.12 | 8.12 | 8.12 | 7.24 | 7.24 | 7.24 | 6.52 | 6.52 | 6.52 | 6 | 6 | 6 | 5.69 | 5.69 | 5.69 | 4.97 | 4.97 | 4.97 | 4.15 | 4.15 | 4.15 | 4.04 | 4.04 | 4.04 | 3.09 | 3.09 | 3.09 | 2.01 | 2.01 | 2.01 | 2.01
Fuel efficiency (km/L)
Truck
Tractor
T1
(Category)
TT2
T2
T3
T4
T5
T6
T7
T8
T9
T10
T11
TT1
The 2025 fuel efficiency standard is 7.63 km / L on average for the all category.
This standard is strengthened by 13.4% compared to 2015 standard.
8

## Slide 10
New fuel efficiency standard for buses (2025 standard)
Chart: 
| 1 | 1.5 | 2 | 2 | 2.5 | 3 | 3 | 3.5 | 4 | 4 | 4.5 | 5 | 5 | 5.5 | 6 | 6 | 6.01 | 6.5 | 7 | 7 | 7.5 | 8 | 8 | 8.5 | 9 | 9 | 9.5 | 10 | 10 | 10.5 | 11 | 11 | 11.5 | 12 | 12 | 12.5 | 13
2025年度基準案 | 7.1474 | 7.1474 | 7.1474 | 6.2978 | 6.2978 | 6.2978 | 5.7971 | 5.7971 | 5.7971 | 5.2876 | 5.2876 | 5.2876 | 4.5279 | 4.5279 | 4.5279 | 9.5402 | 9.5402 | 9.5402 | 7.7343 | 7.7343 | 7.7343 | 6.3659 | 6.3659 | 6.3659 | 6.0608 | 6.0608 | 6.0608 | 5.2906 | 5.2906 | 5.2906 | 5.2778 | 5.2778 | 5.2778 | 5.1385 | 5.1385 | 5.1385
2014年度平均燃費値 | 6.78 | 5.59 | 5.32 | 5.11 | 4.41 | 8.86 | 7.56 | 5.83 | 5.63 | 4.75 | 4.84 | 4.83
2015年度基準 | 6.97 | 6.97 | 6.97 | 6.3 | 6.3 | 6.3 | 5.77 | 5.77 | 5.77 | 5.14 | 5.14 | 5.14 | 4.23 | 4.23 | 4.23 | 9.04 | 9.04 | 9.04 | 6.52 | 6.52 | 6.52 | 6.37 | 6.37 | 6.37 | 5.7 | 5.7 | 5.7 | 5.21 | 5.21 | 5.21 | 4.06 | 4.06 | 4.06 | 3.57 | 3.57 | 3.57
Fuel efficiency (km/L)
Route bus
Tour bus
BR1
BR2
BR3
BR4
BR5
B1
B2
B3
B4
B5
B6
B7
(Category)
2025 standard
2015 standard
average fuel efficiency in 2014
The 2025 fuel efficiency standard is 6.52 km / L on average for the all category.
This standard is strengthened by 14.3% compared to 2015 standard.

## Slide 11
1. Background
2. History of Developing FE Standard
3. Outline of Standard
4. Test Method

## Slide 12
Characteristic of heavy duty vehicles
In heavy duty vehicles, there are many kinds of power train depending on difference of horse power, transmission and differential. There are also many types of body depending on difference of wheelbase and tire size.
In the trucks which account for about 90% of the number of heavy duty vehicles, these are shipped mainly in semifinished state, and the rear body is selected by the user to be a completed vehicle.
Therefore, it is difficult to measure with real vehicles which have many pattern, so in Japan has adopted the test method to calculate fuel efficiency using simulation since 2006.

## Slide 13: Outline of test method
- Payload
- Running resistance
Full Torque Curve
Conversion
&
Calculation
Program
Engine
T/M
F/G, Tire
Vehicle Specification
Gear ratio, Eff.
Gear ratio,Eff.
Dia.
Engine speed rpm
Fuel flow L/h
(Measured)
Torque Nm
Combined
Fuel
Consumption km/L
Fuel
Consumption
- JE05 mode
- High-way mode

## Slide 14
Time (s)
Vehicle Speed (km/h)
縦断勾配 %
High-way mode
８０km/h一定、勾配付
Test cycle and weighting factor
Fuel efficiency of heavy vehicles is calculated by combining fuel efficiency simulated by “JE05 mode" and “High-way mode" at high-way ratio determined for each category.
JE05 mode
Time (s)
Category |  | High-way Ratio | Payload Ratio
Truck | T1 | 15% | 45%
 | T2 |  | 
 | T3 |  | 
 | T4 |  | 
 | T5 | 35% | 50%
 | T6 | 40% | 
 | T7 |  | 
 | T8 |  | 
 | T9 |  | 
 | T10 |  | 
 | T11 | 55% | 55%
Tractor | TT1 | 45% | 50%
 | TT2 |  | 
Route Bus | BR1 | 0% | 35%
 | BR2 |  | 
 | BR3 |  | 
 | BR4 |  | 
 | BR5 |  | 
Tour Bus | B1 | 15% | 60%
 | B2 |  | 
 | B3 |  | 
 | B4 | 45% | 65%
 | B5 |  | 
 | B6 | 55% | 
 | B7 |  | 
Notes: 13
Next, I'll speak about the driving cycles.
Heavy-duty vehicle are used in urban and intercity expressway.
So, both driving cycle have to be examined.
JE05 is representative as urban driving, so, JE05 is decided as urban driving cycle.

## Slide 15
Accuracy of simulation method
y = 0.993x
R
2
= 0.9952
0
2
4
6
8
10
0
2
4
6
8
10
Fuel efficiency by measurement (km/L)
Fuel efficiency by simulation (km/L)
Vehicle A (JE05)
Vehicle A (High-way)
Vehicle B (JE05)
Vehicle B (High-way)
The simulation method adopted as the heavy duty vehicle fuel efficiency measurement method in Japan has a comparatively small error from the measurement on the vehicle base.
Notes: 14
Next, I'll speak about the driving cycles.
Heavy-duty vehicle are used in urban and intercity expressway.
So, both driving cycle have to be examined.
JE05 is representative as urban driving, so, JE05 is decided as urban driving cycle.

## Slide 16
Input data into simulation
Item | Amendment from 2025 standard
Aero drag | Introduction of aerodynamic resistance coefficient of individual car
Tire rolling resistance | Reflecting tire rolling resistance coefficient
Shift Logic | Update shift point
Rotational inertial mass | Equivalent rotating mass inertial mass review
Standard vehicle specifications | Update the standard vehicle specifications
Transient compensation | Introduction of transient compensation coefficient
Fuel consumption map measurement | Increase measuring point
Weighting factor (High-way ratio and Payload ratio) | Update high-way ratio and payload ratio

## Slide 17
1) Aero drag measurement method
How to measure Cd coefficient like coast down, etc with correction using wind flow meter.
→ “Constant speed (with wheel torque meter)” and “Coast down “
“Anemometer” is Option
CFD and wind tunnel. → N/A
Measurement : Aero drag

## Slide 18
1) Tire rolling resistance
How to measure tire rolling resistance. → ISO28580
2)Resistance select method
How to select the rolling resistance.
Unique value of tire or value using ranking of tire.
Measurement : Tire rolling resistance

## Slide 19
1) Steady state engine map
Number of points, measuring order, and measuring process like sweep time and measuring time, etc.
Engine speed 10 ×Torque 5
+ Idling = 51points
Engine speed 6 ×Torque 5
+ Idling = 31points
Current FES
Next FES
Measurement : Engine Map

## Slide 20
Thank you for your attention!