## Slide 1
January 7, 2019
HDV CO2 Regulation in REPUBLIC OF KOREA
Notes: Hello Lady and Gentleman
I’m Yunsung Lim, I have been working in NIER since 2002.
Now I work for CAFÉ and assessment about off-cycle or eco innovation for LDV.
I introduce HDV CO2 eegulation in Rep of Korea.

## Slide 2
Timeline
Model structure
Input & generic data
Simulation accuracy analysis
Future work
Notes: This time presentation contents

## Slide 3
1. Timeline
Notes: The first presentation is timeline

## Slide 4: Timeline
Regulatory Timeline
 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Monitoring
Legislation
Start of Regulation
Simulation model development
Monitoring (2019 ~)
Simulation model distribution to manufacturer (1st distribution in 2016, 2nd distribution in 2017), Input data submission
Start of Regulation (2021 ~)
Legislation (2020)
Set CO2 reduction target, super credit, eco innovation technology, draft regulation
1st
distribution
2nd
distribution
Draft
Notes: Regulatory timeline in South Korea.
We have been researched simulation model for HDV CO2 assessment

## Slide 5
2. Model structure

## Slide 6: Model structure
Simulation model: HES, Heavy-duty vehicle Emission Simulator
Backward type calculation program (wheel to engine)
Vehicle dynamic based simulation model for MHDVs (Medium and Heavy Duty Vehicles) in Korea
MHDVs simulation model (Korea): Composed of five components as follow:
  Pre-processor module: reading input data (vehicle specifications and velocity profile)
  Chassis module: calculating total resistance force acting on vehicle
  Transmission module: predicting gear position at each time step based on engine operating condition
  Engine module: determining engine torque & speed at each time step
  CO2 emission module: predicting CO2 emission based on fuel map & CO2 emission factor of fuel
Chassis
(prediction of
total resistance F)
Transmission
(gear shifting)
Engine
(engine speed, engine torque)
CO₂ emission
(FC map)
Calculation flow
Fig. Basic model structure
Pre-processor
1. Test cycle
(K-WHVC mode)
2. Vehicle spec.
(input data)

## Slide 7
Test cycle (target velocity)
Fig. Comparison of original WHVC and K-WHVC mode (velocity profile)
Modification of WHVC driving mode
WHVC mode represents real driving pattern of MHDVs in Korea reasonably.
However, some HDVs (GVW>30 ton) are not able to follow the WHVC in specific acceleration regions.
K-WHVC driving cycle had been developed to enhance a correlation between simulation and test results.
Model structure
Notes: 참고문헌 : “Review of Power Cylinder Friction for Diesel Engines”, Journal of Engineering for Gas Turbines and Power

## Slide 8
3. Input & generic data

## Slide 9
Input data
Input
3
1
2
4
Engine
Fuel consumption map
Full load curve
3
Transmission
Gear ratio
Gear efficiency
4
Vehicle specification
Weight
Tire radius
Resistance coefficient (f0 / f1 / f2)
idling & max engine rpm
Idling fuel consumption
Engine displacement
Start gear position
Max gear position
Auxilially power demand
1
Driving cycle
JE05 mode
WHVC mode
K-WHVC mode (default cycle)
2
WHVC mode
JE05 mode

## Slide 10
Input data
Vehicle type: MHDVs are divide into five classes
(heavy duty truck, medium duty truck, light duty truck, city bus, ordinary bus)
Vehicle weight: half-loaded
Tire radius: dynamic radius
Road load coefficients (derived by coast down test): F0, F1, F2
Engine displacement
Idle & maximum engine speed
Start gear position: determine 1st or 2nd gear position at start condition
Auxiliary power demand: technology list, Idle stop: Y or N
1. Vehicle specification
2. Transmission specification
Gear ratio: Up to 16th gear
Final gear ratio
Gear efficiency or Torque loss map
Gear type (automatic or manual transmission)

## Slide 11
Input data
Fuel consumption map is used to calculate a fuel consumption & CO2 emission rate of vehicle in whole driving time.
Data composition of fuel consumption map:
- Engine speed (x axis, RPM)
- Engine BMEP (y axis, bar)
- Fuel consumption rate. (z axis, kg/h)
Interpolation method is important to increase prediction accuracy
3. Fuel consumption map
4. Engine full load characteristic curve
Engine full load characteristic curve data is used to calculate a maximum engine torque in whole driving time.
Engine full load characteristic curve data is also used to calculate a normalized torque & torque margin.
Fig. Engine full load characteristic curve
Fig. Fuel consumption map

## Slide 12
Generic data
K-WHVC mode is composed of three phases
- Urban (0-900 sec)
- Rural (901-1,368 sec)
- Motorway (1,369-1,800 sec)
Weighting factor is differently applied at each MHDVs (divided into five classes)
Type | Weighting factor (Urban : Rural : Motorway)
City bus | 9 : 1 : 0
Ordinary bus | 1 : 2 : 7
Light-duty Truck | 2 : 4 : 4
Medium-duty Truck | 1.5 : 3.5 : 5
Heavy-duty Truck | 1 : 3 : 6
Table. Weighting factor for MHDVs of Korea
Fig. K-WHVC test cycle
5. Test cycle & weighting factor
Motorway: 1,369-1,800 sec
Urban: 0-900 sec
Rural: 901-1,368 sec

## Slide 13
4. Simulation accuracy analysis

## Slide 14
Simulation accuracy analysis
Rigid Truck test
Type | GVW (ton) | Max payload (ton) | Displacement (L) | Model year
Rigid truck | 7.2 | 3.5 | 3.9 | 2017
Rigid truck | 10.4 | 4.5 | 6.3 | 2017

## Slide 15
Simulation accuracy analysis
City bus test
Engine | Peak power | Displacement | Weight | Passenger capacity | Transmission | Model year
CNG C6AF | 290 PS | 11.6 L | 13.09 Ton | 54 | Manual | 2017

## Slide 16
Simulation accuracy analysis
HDV simulation
423 HDVs simulation
Diesel HDV 370 cases, CNG HDV 53 cases
Half payload test
K-WHVC simulation (weighting factors of Driving cycle are not applied)
Notes: In previous research, we analyzed as many vehicle as possible by using HES model.
This graph shows the Korea Heavy-duty vehicle simulation results.
423 vehicle specifications are used for simulation calculation.
Red points are diesel simulation results and green points are CNG simulation results.
Diesel heavy-duty vehicles account for 97% of total Heavy-duty vehicles in Korea, and rest of HDVs are CNG buses.
The vehicle specifications, which are used for this graph, are collected by Ministry of Environment before 2015
From this year 2019, we plan to start monitoring on heavy-duty vehicle CO2 emission.
So, more detailed and accurate vehicle data will be used for this kind of research in this year.
Considering monitoring result of this year , we will decide CO2 reduction rate of heavy duty vehicle.

## Slide 17
5. Future work

## Slide 18
Future work
Future work: HDV CO2 Regulation
2019: HDV CO2 emission monitoring
  Vehicle data submission (OEMs)
  Accurate calculation of CO2 emission from HDVs
2020: Legislation process
    Public hearing about CO2 emission regulation
    Determination of CO2 reduction rate
2021: Start of CO2 emission regulation from HDVs

## Slide 19
Thanks for your attention